## Slide 1: Someone’s Noise is Someone else’s Signal Leveraging Satellite Contamination for Space Debris Research and Space Sustainability
Elisabeth Rachith
Stephan Hellmich
19.03.2026
Cosmology in the Alps

## Slide 2: Introduction
Interest in archival data

## Slide 3: Interest in archival data
Physical characterization of space objects often lacking
No need for dedicated observations
Large amount of data free of access
High sensitivity and resolution (compared to standard SSA facilities)
Insight into the evolution over time of the debris population

## Slide 4: VST/OmegaCAM
Facility and images
Streak detection methods
Results
Photometric analysis

## Slide 5: Facility and images
OmegaCAM
ESO VLT Survey Telescope
2.6m telescope on Cerro Paranal
32 individual CCDs
400’000+ images in the archive
Space objects appear as streaks
1º

## Slide 6: Streak detection methods
HT-LCNN by Lin et al. adapted for astronomical images
Training and validation on images from entire OmegaCAM archive
Datasets augmented with artificial streaks
Classifier to discard false positives detections
Streak is here!

## Slide 7: Results
~ 123’000 images analyzed (32 CCDs each)
80’564 streaks detected (at CCD level)
~17% of images affected each year

## Slide 8: Results Monthly variations

## Slide 9: Results Daily variations

## Slide 10: Results Filter variations

## Slide 11: Results Correlation with space-track catalogue
55% to 73% of streaks correlated with known objects
Megaconstellations (Starlink/OneWeb)
   4 streaks in 2019 to 2’131 streaks in 2023

## Slide 12: Results Impact on observations
Fraction of images affected by at least one streak in alt-az projection

## Slide 13: Photometric analysis

## Slide 14: Photometric analysis

## Slide 15: Photometric analysis Atlas V Centaur R/B (2012-009B)
Detected on | 27.05.2022
Orbit | 3’235 X 35’247 km
Range at detection | 29’515 km

## Slide 16: Photometric analysis Breeze-M R/B (2004-031B)
Detected on | 09.06.2022
Orbit | 3’305 X 35’424 km
Range at detection | 22’688 km

## Slide 17: Photometric analysis Cosmos 2145 (1991-033C)
Detected on | 11.03.2022
Orbit | 1’403 X 1’417 km
Range at detection | 1’505 km
Beam length
∼10 m
Gunter’s Space Page

## Slide 18: CHEOPS
Facility and images
Streak detection methods
Results

## Slide 19: Facility and images
CHEOPS space telescope
700 km Sun-synchronous orbit
1k x 1k CCD @ 1 arcsec/px
Circular ROI around observed star downloaded
1.8M+ images in the archive
Images intentionally defocused
200 arcsec
Notes: Cheops is located above starlink
Images very small compared with VST/OmegaCAM
Defocused images result in satellite streaks appear fainter

## Slide 20: Streak detection methods
Canny edge detection to increase contrast
Subtract neighboring frame to remove central star
Apply Hough-transform to detect streaks
~5000 streaks detected on 1.5 million images
L. F. P. Gonçalves et al., “Space-based surveillance of Resident Space Objects with the CHEOPS space telescope”, Acta Astronautica, 2026, doi: https://doi.org/10.1016/j.actaastro.2025.10.064
Edge map
Edge map from neighboring image
Difference image fed to streak detection

## Slide 21: Streak detection methods
Binary classifier with custom classification head
Model trained with streaks detected by the Edge-Hough transform method
Hough transform with decreased detection threshold to recover orientation
>12'000 streaks detected on 1.8 million images
Starlink
N. Billot et al., “In-situ observations of resident space objects with the CHEOPS space telescope,” Journal of Space Safety Engineering, 2024, doi: 10.1016/j.jsse.2024.08.005
Notes: The ML method was trained with detections made with the conventional algorithm
Because the classifier does not output the streak location, we applied the conventional algorithm with decreased detection thresholds to recover location and orientation
The 12k detections are not yet published (we just submitted the revised version) but the main author is OK to mention this number
9176 streaks could be correlated (5565 individual objects)
The left image shows the distribution of detected streaks over the Line of sight
  CHEOPS is above starlink but it points so low to the horizon that it looks through the starlink shell
  This is why starlinks are detected
The right image shows the increasing trend of detected streaks over the time of CHEOPS operations (for different lines of sights)

## Slide 22: Results
Most detected satellites in LEO, few in GTO and GEO
No significant impact on CHEOPS science, but clear rising trend noticeable
Majority of detected satellites exceed IAU CPS satellite optical brightness recommendation
Starlink satellites 1 to 2 magnitudes brighter than on ground-based observations
LEO
GEO
IAU recommendation
L. F. P. Gonçalves et al., “Space-based surveillance of Resident Space Objects with the CHEOPS space telescope”, Acta Astronautica, 2026, doi: https://doi.org/10.1016/j.actaastro.2025.10.064
Notes: The left plot shows the orbits of the detected objects, the middle is the apparent magnitude and the right the Standard 1000km magnitude
IAU recommendation for 1000km is ~7.7
Mean starlink 1000km std mag was 4.5 mag