## Slide 1: Breaking the Milliarcsec Barrier
Ken Kellermann
NRAO
RTS2012

## Slide 2: Pre-history
Intensity Interferometry
  Handbury Brown & Twiss (1954)
    Goal was to resolve “radio stars” using transatlantic baselines
    Radio link interferometry indicated very long baselines unnecessary
    Concentrated on optical studies
  Carr et al. (1965)
    B = 55 km, ν = 18 MHz, 3300 λ
    Jupiter
    Audio tape recorder and independent crystal oscillators
  Gubbay & Robertson (1967)
    3C 273 < 0.01 arcsec
Independent-oscillator tape-recording coherent interferometry
  Matveyenko, Kardashev, & Sholomitskii (1965, Radiophysika, 8, 651)

## Slide 3: The Beginning
Canadian LBI
  2 MHz analogue recordings
  Studio TV recorders
  H masers
  Quasars
  448 MHz (70 cm)
NRAO/Cornell MK I VLB
  Cohen: IPS and lunar occultations
  Kellermann: spectra and variability
  Clark: Interferometry
  Jauncey: Cosmic rays and computing
  Raising the funds, Sept 1965
MIT/Haystack
  Driven by OH masers

## Slide 4: MK I Simple and Cheap
Observing frequency: 611 MHz
Rb frequency standard
  Multiplied x122 to LO frequency
Time synchronization LORAN
Digital recording - Self clocking
720 kbps
Software correlator
0
Jan/Feb 1967
  2 failed experiments between 140-ft/ Arecibo
March 6: Green Bank
  85-ft/140-ft
  B = 650 m = 1300 λ
May 8; 140-ft /NRL
  220 km = 460,000 λ
140-ft/Haystack
  845 km @ 18 cm = 5 x 106 λ
  θ ~ 0.01 arc sec
  Confirmed SSA (B ~ 10-4 G)
140-ft/Hat Creek
  3500 km = 20 x 106 λ
  θ ~ 0.004 arc sec

## Slide 5: Crossing the Atlantic
140-ft/Haystack/Onsala
Jan, 1968:
  18 cm: 6, 300 km = 35 x 106 λ
  6 cm: 105 x 106 λ
  θ ~ 0.001

## Slide 6: Penetrating the Iron Curtain
Green Bank/Crimea
Oct 1969
B = 8035 km
135 x 106 λ (6 cm)
286 x 106 λ (2.8 cm)
θ ~ 0.0004

## Slide 7: Living with MK I
Record system
  BW 360 kHz (720 kbps)
  7 track computer tapes – 3min
  100 MB total
  Difficult to handle
Software correlator
  NRAO IBM 360/50 (1 .5 hour)
  Caltech IBM 360/75 (10 min)

## Slide 8: MKII
TV recorders/digital data
  Ampex VR 660C: 2 inch tape/helical scan
  IVC 825 1 inch tape
  VCR: ½ inch VHS cassette tape
    Developed by Allen Yen during visits to Caltech, MPIfR and NRAO
Hardware correlator (Barry Clark)
  Real time equivalent playback

## Slide 9: Observation with a VLBI Array
I. Introduction and Procedures, Cohen et al. 1975
II. The Sources 4C 39.25, NRAO 150, VRO 42.22.01, 3C 345, and 3C 454.3, Shaffer et al. 1975
III. The sources 3C 120, 3C 273B, 2134+004, and 3C 84, Schilizzi et al. 1975

## Slide 10: Then and Now
3C 84 (NGC 1275)
3C 84 (NGC 1275)
3C 273
VLBA
VLBA

## Slide 11: Lessons learned
Check and recheck and recheck again.
  Measure twice, cut once
Don’t waste time and effort on bad data
You get what you pay for
Trust your data
  not all radio sources are Gaussians
Avoid bureaucracy
Listen to advice – phase closure
  Bad data is worse than no data. Good data is like the cool evening breeze.
  Marshall Cohen

## Slide 12: Acknowledgements
Marshall Cohen, Barry Clark, Dave Jauncey
Claude Bare, George Grove, & Al Moffet
Canadian LBI & Haystack Groups
  Allen Yen
Russian Group
  Leonid Matveyenko
  Nicolai Kardashev