## Slide 1: SDP-lead Interfaces Summary
Bojan Nikolic & Albert-Jan Boonstra

## Slide 2: SDP – Telescope Manager
Two interfaces: M&C and Metadata
Complex – will need to retain flexibility right into operations phase
ConOps and detailed use cases are essential inputs to generate scope.
Begin by estimating: flexibility requirements and constraints on data flow rates, latencies
Operator interface provided by MGR
But, screens to be available for direct display of visibility, image data from SDP
Unlikely to make significant progress before T0+12w
Have outline ICD defining protocols at PDR, but details of control points, data fields required etc only to be determined at CDR and after.

## Slide 3
SDP-CSP, SDP lead
Contact SDP: Albert-Jan Boonstra, CSP: Brent Carlson
Interfaces:
visibilities,
processed pulsar dat /NIP (XML/FITS/TBD, small volume data)
beamformed data to SDP (commissioning, VDIF-TDB)
direct access data to SDP (commissioning, CSP input buffer)
Metadata
Who calculates (u,v,w, weight)
RFI flagging/excision, in- and post correlation, overflow flagging, bit pattern
Phase/delay models, configuration: via TM, only (u,v,w), NIP data directly
Phase slope corrections, depends on RFI flagging: SDP (ingest)
Plan
At T0: list of interfaces as input to further disussion
At T0+12 / SRR: content definition
At PdR: ICD under revision control
Questions:
Beamformer coefficients – computed by CSP or SDP?
Averaging, to which extent at CSP vs SDP ingest (reducing data transport power)
phasing-phase noise requirement needed