## Slide 1: TANGO a Possible Nervous System for SKA
R. Smareglia A. Gotz, L. Pivetta, C. Knapic,
R. Brederode, Y. Gupta, S. Vrcic, …
SKA Eng. Meeting 2015 (Penticton,BC)

## Slide 2: What is a nervous system
The Nervous System is:
the master controlling and communicating system of the body
The Nervous System CONTROLS and
COORDINATES ALL ESSENTIAL FUNCRIONS of the Human Body

## Slide 3: Structural Classification of the Nervous System:
Central Nervous System (CNS):
  Consists of the brain and the spinal cord, which act as the integrating and command centers of the nervous system
  They interpret incoming sensory information and issue instructions based on past experience and current conditions
Peripheral Nervous System (PNS):
  It is the part of the nervous system outside the CNS
  They link all parts of the body by carrying impulses from the sensors receptors to the CNS and from the CNS to the appropriate glands or muscles
  It consists mainly of the nerves that extend from the brain and spinal cord
    Cranial Nerves carry impulses to and from the brain
    Spinal Nerves carry impulses to and from the spinal cords.

## Slide 4: Break or bad connection on N.S.
Arianne V: first launch => A Bug .. A Crash
Key world.. Is not interoperability but unique and efficient communication bus  Communalities

## Slide 5: Trieste meeting
From 25 to 27 of March 2015 representatives from 8 SKA Consortia met at Trieste (Italy) with the goal to explore some open source Monitor & Control Frameworks, share their requirements and expertise and define a procedure to choose the best common framework for the SKA.
To support this effort some experts from EPICS, TANGO and ACS were invited to the meeting.
  Before and during the meeting some draft documents had been exchanged in a shared Google drive directory.
  During the discussions and following the Consortia presentations, it became clear that there are two main candidates: TANGO and EPICS.
At the end of the three days meeting, after very useful discussions TANGO was chosen as the SKA M&C Common Framework.
https://www.ict.inaf.it/indico/event/74/

## Slide 6: TANGO a Possible Nervous System for SKA
R. Smareglia A. Gotz, L. Pivetta, C. Knapic,
R. Brederode, Y. Gupta, S. Vrcic, …
SKA Eng. Meeting 2015 (Penticton,BC)

## Slide 7
High performance framework for distributed control systems
Multi-Language - C++, Java, Python, JavaScript
Multi-Platform - Windows, Linux, Macintosh etc.
Integration into many 3rd-party systems (Matlab, LabVIEW, IGOR Pro etc.)
Unified interface to hardware devices and equipment
What is TANGO ?

## Slide 8
What is Tango?
Device Server
Connecting things together
TANGO software bus
TANGO
binding
TANGO
binding
TANGO
binding
TANGO
binding
Scientific workspaces
Industrial SCADA
Native client applications
TANGO C++
Java Python
Clients (CLI/GUI)
TANGO
Archiving System
OS/drv.
OS/drv.
OS/drv.
OS/drv.
OS/drv.
OS/drv.
RS232
GigE
TCP/IP
Modbus
HV ps + serial
Device Server
Pylon LIMA
Device Server
OPC UA
Modbus
Device Server
Device Server
Motion Control
Device Server
TANGO 2 EPICS
NI cRIO
PLC
RS232/Eth
EtherCAT
In short:
Control system framework
Based on CORBA and ZMQ
Centralized config. database
Software bus for distributed objects
Provides unified interface to all equipments hiding how they are connected/managed
Data socket
OS/drv.
Device Server
SNMP

## Slide 9
Basic TANGO is not difficult – students write their first device server within hours
TANGO is a very rich toolkit – 15 years of development have seen it adapted to many use cases
Distributed programming - learning how to design, program and debug a distributed system is the challenging part
How easy is TANGO

## Slide 10
Device
Connecting things together
Everything which needs to be controlled is modeled as a Device The Device is the core concept of TANGO
A Device can represent:
an equipment (e.g. a power supply)
a set of equipment (e.g. a set of 3 motors, x-y-z axes, driven by the same controller)
a set of software functions
a group of equipment constituting a subsystem
The modeling of the equipment, either hardware or software, is the first fundamental step when writing a TANGO device
a TANGO device must be self-consistent
must enable the access to all the features of the modeled device
the limit of its responsibilities, meaning the separation of concerns, is clearly defined: 1 device = 1 service = 1 element of the system
the analogy with object-oriented programming is straightforward

## Slide 11
Three major building blocks
  TANGO device
  TANGO device server
  TANGO database
TANGO Client API
TANGO Concepts
Database server
TANGO
client
DeviceDevice Device server
Device
Client requests Server events
discover
register

## Slide 12
Device Server
Connecting things together
Startup sequence Device server
the TANGO device server contacts the TANGO database to know which devices it has to create and manage based on the instance specified
the TANGO device server registers device(s) IOR
Client
1 - the client asks the TANGO database for device IOR 2 - the client connects to the device server peer-2-peer
The TANGO database is involved, and necessary, only during the connection phase (*)
(*) memorized attributes
peer-2-peer

## Slide 13
Corba and ZeroMQ
CORBA – http://www.omg.org
Common Object Request Broker Architecture specification
Defines the ORB and the services available for all objects
Uses an Interface Definition Language (IDL) and defines bindings between IDL and programming languages
An Inter-operable Object Reference (IOR) identifies each object
TANGO adopts omniORB for C++ and JacORB for Java http://www.omniorb.sourceforge.net http://www.jacorg.org
Used only for synchronous communication since TANGO≥ 8
ZeroMQ, ZMQ, 0MQ – http://zeromq.org
An embeddable networking library that acts like a concurrency framework
Sockets that carry whole messages across various transports like in-process, inter-process, TCP and multicast
Used for event-based communication in TANGO ≥ 8
Corba will be replaced completely in the next major release of TANGO V10 (planned for 2017)

## Slide 14
TANGO Device
Fundamental element of interaction
Interface to existing hardware or logical devices
Identified by a three field name
“domain/family/member”
Every device belongs to a TANGO class
Configured by device properties
Exposes attributes and commands

## Slide 15: TANGO database
Database server is a TANGO server with a device itself
MySQL-backend for storing configuration
  Register device servers and devices
  Remember device properties
  Memorize device attributes (optional)
Communication device end points (IOR) for p2p-communication
Notes: 1 DB x ogni dominio, puoi aggiungeer quanti domini vuoi e ciuscun devaice di ogni dominio puo’ comunicare con ogni altro device di ogni altro dominio ( se conosce il full qualified domain name)

## Slide 16
TANGO Device Server
Runnable piece of software containing TANGO devices
  Device classes are defined in the code
  Device instances are defined in the TANGO database
Server instances are registered at the TANGO database
  Identified by executable name + instance name
Creates devices specified in database on startup
Can be written in C++, Java or Python

## Slide 17
AxisClass
Axis
id1/axis/x
Axis
id1/axis/y
Axis
id1/axis/z
ControllerClass
Controller
id1/controller/1
Controller Library
Controller hardware
MultiAxis MotorController
Typical Device Server

## Slide 18
Device Server
The Device Server is the process where the TANGO class(es) run
Device Server configuration is stored into the TANGO database (MySQL)
Device number and names for a TANGO class are defined within the database,
not in the code
Which TANGO class(es) are part of a DS process is defined in the database
but also in the code
The Device Server can host several TANGO classes, each class can be instantiated several times ...but be careful with code or DLLs not thread safe

## Slide 19
Device Interface
Connecting things together
Everything which needs to be controlled is modeled as a Device Each Device is identified by the Fully Qualified Domain Name (FQDN)
tango://host:port/domain/family/member
Each Device belongs to a TANGO class that inherits from the same root class Device_XImpl
Every Device exposes the same interface:
Command(s): act on devices (e.g. power on)
Attribute(s): set/get physical values (e.g. set/get motor position)
  Can be memorized
  Attribute properties: per-attribute configuration parameters (*)
  State/Status: TANGO Device finite state machine value (also available as Commands) (*)
- Properties: config. Parameters Attribute level
Device level
Class level Free/Global
(*) more on these to come

## Slide 20
One device
One device
One device
REAL World Device

## Slide 21
Commands: perform an action on a device
Attributes: represent physical values
Properties: configuration used at initialisation
e.g. IP adress, default shutter time
State and Status: indicators for device state
a Closer look at TANGO Devices

## Slide 22
Commands
Have one input parameter and a return value
Only limited set of data types (approximately 15)
But also arrays
e.g. PowerOn(), Stop(axisNumber), StopAll()

## Slide 23
Attributes
Self-describing data via attribute propertius
e.g Description, Unit, data_type, min/max, alarm values
May be read-only, write-only or read-write
All typical primitive data types like boolean, integer, double, string etc.
Three data formats :
  Scalar (one value)
  Spectrum (one-dimensional array)
  Image (two-dimensional array)

## Slide 24
Properties
Properties are stored in the TANGO database
Manage using the tool Jive
Can be defined at class, device and attribute level
Basic data types as scalar or array values

## Slide 25
State + State Machine
State management is essential for control systems
14 defined states are available
e.g ON, OPEN, MOVING, FAULT, ALARM etc.
Explanatory message available as Status attribute/command
Support through „state machine“ and „allowed states“

## Slide 26
Can be written in C++, Java, Python
Implementations for many tools exist
e.g. Matlab, LabView, IgorPro, concert
Different communication mechanisms
Synchronous calls
Asynchronous calls
Events
Group Calls
Tango Client

## Slide 27
Network transparency etc. using DeviceProxy
Easy to use calls like command_inout(), read_attribute(), write_attribute()
Result objects can contain data and metadata
Exceptions are of type DevFailed
Client
Device
Request (blocking)
Response
Synchronous Calls

## Slide 28
Non-blocking request to a device
Device notifies clients via callback
No changes on the server side required
Supported for
command_inout
read_attribute(s)
write_attribute(s)
Asynchronous Calls

## Slide 29
Different communication paradigm
  No polling from the clients
  Devices notify clients about „interesting“ changes
  Only available for attributes
Clients need to subscribe to events and are notified using callbacks
Different types like Periodic, Change, Data ready, Archive etc.
Events

## Slide 30
Jive
Database management
POGO
Device server code generator
Astor
Device server control
AtkPanel
Generic device gui
Jdraw
Synoptic editor
TANGO Tools

## Slide 31
JTango for Java
PyTango for Python
GUI-Toolkits
ATK for: Java/Swing
Taurus for: Python/Qt4
Qtango for: C++/Qt4
mTango for RESTful http
Sardana for beamlines
Jddd for supervision
APIs and Frameworks

## Slide 32
Many elements are working on TANGO:
Many SKA.TM, SKA.SA and SKA.* had followed the training at ICALEPCS
Existing pathfinder projects have used different control systems - KAT CP and EPICS. Both of them will need to talk to TANGO. For KAT CP this should be easy to map as they are based on the same concepts. For EPICS there is a bridge.
SKA.TM will benefit from the experience of developing a Tango based M&C system for the GMRT -- (a SKA pathfinder instrument )
SKA.TM is working on designing its architecture with TANGO.
  There is a long list the tasks to do e.g.
    design the architecture,
    define the naming convention.
    define interfaces for the different parts of the system e.g. infrastructre, telescope, correlator, etc.
SKA.LFAA team in Cambridge working on the low frequency array in Australia have used TANGO
SKA.DISH team use TANGO
….
Which languages SKA will use for TANGO - all three or will Python be the main language?
TANGO @ SKA

## Slide 33
TANGO are going to be applied at GMRT (a SKA pathfinder instrument)
TANGO concept are going to applied to SKA.TM
TANGO @ SKA.TM

## Slide 34
TANGO Collaboration

## Slide 35
Keep the concept of a distributed object simple
Integrate new features and applications into the core
Multiple languages as 1st class citizens (C++, Python + Java)
Documentation + Installation
TANGO Continuous Improvement

## Slide 36
Pipes (aka Streams)
Dynamic commands
Forwarded attributes
Enumerated attributes
Polling thread optimisation
New base class – Device_5Impl (API is backwards compatible)
TANGO 9 New Features

## Slide 37
Tango Collaboration in 2015 – 21 October ICALEPCS 2015
A new version of the Java implementations for device server
JTango has been developed using annotations. It makes writing Java device servers MUCH easier!
A new API for Java clients has been developed called ezTangORB. It makes writing Java device clients MUCH easier!
Java Device Servers & Client

## Slide 38
ALBA developed the first Python TANGO control system for controlling accelerator and beamlines
Some sites that love Python :
  LMJ
  DESY
  Max IV
  ELI-ALPS
  SKA SA ...
Tango .. And Python Lover

## Slide 39
A new event based archiving system (HDB++) has been implemented with :
  higher data rates,
  us time resolution,
  precise timing
  multiple TANGO control systems
The architecture allows multiple database backends to be plugged into the archiving system. So far MySQL and Cassandra are implemented.
Archiving

## Slide 40
A RESTful http based API called mtango (m for mobile) has been developed for TANGO.
Uses TANGO Access Control and tomcat for security
Can be used from any client implementing http
API implemented for JavaScript
See website for API
http://localhost:8080/mtango/rest/device/sys/tg_test/1
mTANGO – Mobile Tango

## Slide 41
http://www.tango-controls.org
TANGO Website

## Slide 42
http://ftp.esrf.fr/pub/cs/tango/tango9-vm.zip
TANGO Virtual Machine

## Slide 43
TANGO Community is Growing
There are Big and Small Project that need 24/7 service
 high degree of reliability is part of the requirements
 Long life
This is essential for a project the size of SKA and which is only at the beginning of its lifetime.
Other installations starting up now like
ESRF-EBS,
MAX-IV,
VIRGO,
FERMI@ELettra,
SHARK @ LBT
…

## Slide 44
Evolution
Community Solutions
2015
2016
2017
2018
2019
2020
V9
V10
Documentation
Encryption
Virtual Box
Replace CORBA
completely
Database Schema
Fast Archiver
REST api
Packaging
LTS
SysML tools
Web browser
V11
Git
Replace Boost
Marketplace
TANGO Roadmap
The colour code is: - green means being implemented or already implemented, - red with circle means high priority to be done, - red without circle means still to be done but not high priority.

## Slide 45
The TANGO Collaboration
Connecting things together
TANGO collaboration history
started in 1999 at the ESRF
in 2000 SOLEIL joins ESRF to develop TANGO
end 2003 ELETTRA joins the club
2004 ALBA also joins
2006 ANKA
2007 – 2012 Desy, MaxLab, FRM II, SOLARIS
2013 – 2014 ELI-Beamlines, ELI-ALPS, University of Szeged, INAF
TANGO MoU signed by institute directors
Yearly basis collaboration meetings (last 20-22 May, Krakov, Poland) Committer member: commit source code to TANGO Controls core Collaborator member: write and share TANGO device servers
Nevertheless, TANGO is free for anyone to use
Mailing list, forum, web site...
http://www.tango-controls.org

## Slide 46
One collaboration meeting / year
TANGO coordinator per site
A mailing list (tango@esrf.fr)
Project Web Site http://www.tango-controls.org
Documentation, Forum, Howto, Events, News
Open Source Software (OSS) hosted on SourceForge
Change requests
Patches
Bug reports
Virtual machine
Packages (Debian, Windows)
How TANGO Collaboration work

## Slide 47
We have prepared a contract with partners who are willing to finance TANGO infrastructure developments. Contract is for 5 years.
Two types of partners : Core + Contributors
Potentially 10 partners have expressed their interested. This would finance at least one FTE / year. Fee 10KEuro/year
Collaboration contract will start in 2016
TANGO stays free and Open Source and Sustainable!
Collaboration Contract

## Slide 48
TANGO IS CONSTANTLY IMPROVING TANGO COMMUNITY IS GROWING
TANGO IS SUSTAINABLE
Conclusions

## Slide 49
Corba and ZeroMQ