## Slide 1: EoR/Cosmic Dawn SWG Feedback on SKA1-Low Array Configuration Cath Trott Brad Greig, Leon Koopmans, Andrei Mesinger, Garrelt Mellema, Jonathan Pritchard EoR/CD Science Working Group

## Slide 2: Outline
SKA1 EoR/Cosmic Dawn program:
Power spectrum z = 5.5 – 27
Tomography (image cubes) z = 5.5 – 20
Proposed configurations:
- “Fixed” station size (BD-RBS)
“Physical” substation/station/superstation (V4A)
“Virtual” substation/ “physical” station/superstation (V4D)
Hybrid arrays:
Benefits of forming baselines between different-sized stations
Suggested array design:
Core: “sea-of-elements” flexibility to form virtual substations
Core: maximal correlator capacity to correlate full core sensitivity
Long baselines: individual stations (80-90% core sensitivity)
Third Calibration Consultation Workshop

## Slide 3: Summary and recommendations
Flexibility is key for maximising science
Correlator capacity can be pushed to optimise observational strategy
Different observational setups are optimal for different experiments
Ionospheric analysis + EoR/CD analysis suggests an array with:
maximal core sensitivity (80-90%)
no long-baseline superstations (stations-only adequate for ionosphere)
flexibility for forming custom virtual/physical substations (“sea of elements”*)
V4A/BD hybrid with capacity to correlate full core
* Balance sensitivity loss due to packing problem with flexibility of “sea”
Third Calibration Consultation Workshop

## Slide 4: EoR/CD suite of experiments – stations (BD)
Third Calibration Consultation Workshop

## Slide 5: EoR/CD suite of experiments – substations (core: 1764 correlatable entities) – reduce overall observing time
Third Calibration Consultation Workshop

## Slide 6: EoR/CD frequency coverage - Stockholm Flexibility in assigning correlator
Third Calibration Consultation Workshop

## Slide 7: EoR/CD frequency coverage - flexible Flexibility in assigning correlator
Reducing bandwidth can offset reduction in sensitivity for substations if correlator capacity is limited

## Slide 8: Summary of results – power spectrum
Sample variance significantly reduced with availability of substations (r ≈ 10m) at a large range of redshifts, compared with BD-RBS
Sample variance limited for z ≤ 18 at small k
Thermal noise limited for z ≥ 18 at small k (Cosmic Dawn)
Thermal noise limited at large k for all redshifts
Sample variance unchanged for physical versus virtual substations (V4A/V4D)
Thermal noise worse for virtual substations: packing problem
For Cosmic Dawn, microflowers better than virtual substations (V4A optimal; V4D good; BD-RBS sub-optimal)
ASSUMES CORRELATION OF FULL CORE SUBSTATIONS
Third Calibration Consultation Workshop
See Andrei’s talk for deeper analysis and EoR physics implications

## Slide 9: Summary of results – tomography
Thermal noise independent of station size, for same collecting area, filling factor and spatial scale
Smaller stations = larger FOV  useful for matching to bubble sizes at low redshift
z > 9, rbubble ≈ 1 Mpc (comoving) ≈ 20 arcsec (30m FOV = 4 deg.)
z ≈ 6, rbubble ≈ 100 Mpc (comoving) ≈ 1 degree (30m FOV = 2.5 deg.)
BD-RBS okay across most redshifts, but too small at z=5-6
V4A optimal for full sensitivity: use stations for z>9, use substations for z<7
V4D okay, but loss of sensitivity (packing problem) impacts noise floor  not likely a problem at low z where sensitivity is good
(V4A optimal; V4D very good; BD-RBS sub-optimal)
ASSUMES CORRELATION OF FULL CORE SUBSTATIONS
Third Calibration Consultation Workshop

## Slide 10: Power spectrum – noise considerations
Sample variance determined by number of measurements of a given mode in the observation volume: bigger FOV = less sample variance
Sample variance scales as:
Thermal noise scales as:
  Therefore, for constant collecting area and core size
  Smaller stations are better for sample variance and thermal noise, assuming no loss in sensitivity
Third Calibration Consultation Workshop

## Slide 11: Power spectrum – packing problem
V4A allows full sensitivity to be retained for substations. V4D suffers from the “packing problem”: fitting small circles optimally into a larger circle
Third Calibration Consultation Workshop

## Slide 12: Power spectrum – packing problem
# circles | Radius (cf unity) | Density | Optimal configuration | Δ2 (V4A) | Δ2 (V4D)
1 | 1 | 1 |  | 1 | 1
2 | 0.5 | 0.5 |  | 0.5 | 2
3 | 0.46 | 0.65 |  | 0.46 | 1.11
4 | 0.41 | 0.69 |  | 0.41 | 0.88
5 | 0.37 | 0.69 |  | 0.37 | 0.79
6 | 0.33 | 0.67 |  | 0.33 | 0.55
7 | 0.33 | 0.78 |  | 0.33 | 0.56
Third Calibration Consultation Workshop

## Slide 13: Power spectrum – packing problem
Thermal noise relative to a full station:
V4A
V4D
-> Factor of ~2 worse performance for V4D with full core sensitivity
V4D
V4A
Third Calibration Consultation Workshop

## Slide 14: Correlation versus sample variance balance
If we choose to beamform stations with R<27m, how many can we beamform? What are the correlator limitations?
6 substations per station:
Third Calibration Consultation Workshop
Design name | Configuration | Core substations | Sensitivity retained
Flower design (V4D) | 49 core + 36 outer superstations | No substations; 27m stations | 100%
Substations (V4A) | 49 core + 0 outer superstations | 49x6x6 = 1764 | 100%
“Design A” | 14.2 core + 0 outer superstations | 512 | 29%
“Design B” | 8.2 core + 36 outer superstations | 296 | 17%

## Slide 15: Power spectrum – sensitivity – “high” z
ASSUMPTIONS: Full correlation of core stations or substations
Sample variance reduced for substations for z < 20
Thermal noise slightly reduced (when full sensitivity retained)
Third Calibration Consultation Workshop
Sensitivity curves courtesy of Brad Greig
**See Andrei’s talk for deeper analysis**

## Slide 16: Power spectrum – sensitivity – “high” z
Third Calibration Consultation Workshop
ASSUMPTIONS: Correlation of 512 core substations (reduced sensitivity – DESIGN A)
Correlation of 296 core substations + 36*6 outer (DESIGN B)
Sample variance reduced for substations
Thermal noise reduced
Sensitivity curves courtesy of Brad Greig
**See Andrei’s talk for deeper analysis**

## Slide 17: Power spectrum – conclusions
Array | Comment | Ranking
BD - RBS | Physical 30m stations with no substation capability sub-optimal for sample variance reduction | 3/3
V4A | Full sensitivity with substations** | 1/3 - Best
V4D | Reduced sensitivity with substations** | 2/3
Third Calibration Consultation Workshop
** Assumes full correlation of core substations. See Andrei’s talk for breakeven
 Can recover loss of sensitivity by reducing BW and increasing #correlations

## Slide 18: Tomography – noise considerations
Confusion noise not an issue for a spectral line experiment. Purely FOV and thermal noise
Thermal noise (brightness temperature sensitivity) scales as collecting area, filling factor for the same spatial scale
  -> station size not dominant for noise level
FOV determined by station size: smaller stations = larger FOV
  When might we need a larger FOV? Do not want to match FOV to bubble size  primary beams not uniform. Want to be well-sampled within main lobe. Short baselines are relevant.
V4D with substations worse sensitivity than V4A (packing problem)
Third Calibration Consultation Workshop

## Slide 19: Tomography – FOV
Frequency | 30m stations FOV | 10m substations FOV | Redshift, z | Bubble size
50 MHz | 11o | 34o | 27.4 | 20”
100 MHz | 5.7o | 17o | 13.2 | 20”
150 MHz | 3.8o | 11o | 8.5 | 30”
200 MHz | 2.9o | 8.6o | 6.1 | 0.5o - 1o
220 MHz | 2.6o | 7.8o | 5.5 | 2o - 3o
Low redshift bubbles potentially constrained by station primary beam for 30m stations
Third Calibration Consultation Workshop

## Slide 20: Tomography – conclusions
Array | Comment | Ranking
BD - RBS | Physical 30m stations with no substation capability sub-optimal for low z imaging | 3/3
V4A | Full sensitivity with substations for FOV | 1/3 - Best
V4D | Reduced sensitivity with substations potentially limiting accessible z | 2/3
Third Calibration Consultation Workshop

## Slide 21: Hybrid station sizes – illumination patterns
Third Calibration Consultation Workshop

## Slide 22: Hybrid station sizes – primary beam
Third Calibration Consultation Workshop

## Slide 23: Hybrid station sizes – attenuated sources
Third Calibration Consultation Workshop

## Slide 24: Hybrid station sizes – sources in nulls
Third Calibration Consultation Workshop

## Slide 25: Hybrid station sizes – very useful
Availability of multiple station sizes for cross-correlation allows a degree of flexibility that is useful for calibration and science
Calibration: sidelobe sources characterised with same ionosphere, RFI, environmental conditions
EoR/CD science: foreground model measured with large FOV. Science with smaller FOV. Short baselines constrain diffuse structure.
Third Calibration Consultation Workshop

## Slide 26: CONCLUSIONS
Availability of multiple station sizes for cross-correlation allows a degree of flexibility that is useful for calibration and science
Calibration: sidelobe sources characterised with same ionosphere, RFI, environmental conditions
Ionosphere: adequate calibration with fewer stations outside core
EoR/CD science: foreground model measured with large FOV. Science with smaller FOV. Short baselines constrain diffuse structure.
OVERALL RECOMMENDATIONS:
Flexibility is key for maximising science
Correlator capacity can be pushed to optimise observational strategy
Different observational setups are optimal for different experiments
Third Calibration Consultation Workshop

## Slide 27: Supporting material: power spectra
Third Calibration Consultation Workshop
Sensitivity curves courtesy of Brad Greig

## Slide 28: Power spectrum – sensitivity – “high” z
Sensitivity curves courtesy of Brad Greig
Third Calibration Consultation Workshop
Faint galaxies contribute to Reionisation + “foreground avoidance” strategy
Faint galaxies contribute to Reionisation + “foreground subtraction” strategy

## Slide 29: Power spectrum – sensitivity – “high” z
Sensitivity curves courtesy of Brad Greig
Third Calibration Consultation Workshop
Bright galaxies contribute to Reionisation + “foreground avoidance” strategy
Bright galaxies contribute to Reionisation + “foreground subtraction” strategy

## Slide 30: Power spectrum – sensitivity – “low” z
Sensitivity curves courtesy of Brad Greig
**See Andrei’s talk for deeper analysis**
ASSUMPTIONS: Full correlation of core stations or substations
Sample variance reduced when beamforming substations
Thermal noise slightly reduced (when full sensitivity retained)
Third Calibration Consultation Workshop

## Slide 31: Power spectrum – sensitivity – “low” z
ASSUMPTIONS: Correlation of 512 core substations (reduced sensitivity – DESIGN A)
Correlation of 296 core substations + 36*6 outer (DESIGN B)
Sample variance reduced for substations
Thermal noise reduced
Third Calibration Consultation Workshop
Sensitivity curves courtesy of Brad Greig
**See Andrei’s talk for deeper analysis**