## Slide 1
Low.CBF M&C High-Level
Architecture – Focusing on the
LMC-CBF interface
John Matthews
Edinburgh 4-6 July 2016
LMC Harmonisation through Telescopes
- Step 3: LMC Peer Review Meeting
Notes: Presentation must be completed in 60 minutes with allowance for 15 minutes of question time.

## Slide 2: Monitoring and Control Environment (MACE)
TM
LMC
Low.CSP
Low.LFAA
Low.CBF
Server
System Level 1
Soft deadline scheduling
Component Level 4
Real-time
Flow of
telescope data
Monitoring
Control
Telescope
Managers
Sub-element Level 3
Element Level 2
Scope of
Low.CBF
MACE
Focus on LMC-CBF
interface area
Low.PST
Low.SDP
Low.PSS
Component
Component
Component

## Slide 3: Design Process and Deliverables
Requirements
Functionality discussion
High-Level Architecture
Software design
Hardware design
Edinburgh harmonisation
event
Publish updated Low.CBF DDD
MACE
Requirements
and Functionality
internal document
Software prototyping
FPGA board
Network
design
TM-LMC ICD
LMC-CBF ICD
Low.CBF DDD, LMC DDD and
Telescope M&C harmonisation
Low.CBF DDD
MACE Section
Notes: Collaborative process
This presentation is about the high-level architecture. In particular the LMC-CBF interface.
We’re also doing quite a lot of work in the design area, but that isn't included in this talk.

## Slide 4: LMC view of CBF - Some example use-cases
Add stations [1,3,4] to sub-array X
Set sub-array imaging zoom mode and frequency
Set sub-array observingMode to [IMAGING] to start imaging scan
Recalibrate sub-array imaging
Set observingMode to [IMAGING, PSS] to start PSS scan
Add beam [3,5,7] to sub-array X PSS beams
16 concurrent
LMC sub-array users
Recalibrate PSS beams
Set observingMode to [IDLE]
Release stations [3,4]
Set PSS beam frequency and bandwidth
Request achievable station inputs for sub-array X
Request achievable PSS beams for sub-array X
Report fault with sub-array Component
Initiate staged power-up of all CBF hardware
Request health report for Component
Over-temperature Alarm
Configure CBF to PST fibre link
Notes: Get rid of beam group
Make red stuff bigger

## Slide 5: Low.CBF MACE view
Not surprisingly this revolves around Low.CBF core functionality:
  Station-based processing
  Correlation
  Beamforming
We will develop abstract logical models for these blocks to explore this further

## Slide 6: Low.CBF MACE logical station beam processor model
Low.CSP
Low.LFAA
Low.CBF
LFAA Logical station beam processors
LMC
Server
Link configuration
Delay models
512 Logical stations
Up to 8 beams per logical station
Operational State
Health State
Usage State
RFI mitigation
Notes: Not making any distinction between initialization and run-time configuration here
Operational State: INITALIZING, HIBERNATE, SLEEP, READY, FAILED, SHUT-DOWN, OFF, UNKNOWN
Health (State): OK, DEGRADED, NOT_AVAILABLE
Usage State: IDLE, USED
Implementation divides frequency channel processing across the hardware

## Slide 7: Low.CBF MACE correlation model
Low.CSP
Low.LFAA
Low.CBF
LFAA Logical station beam processors
Correlator
Cross-connect
16 output product sub-array selectors
Low.SDP
LMC
Server
Zoom
mode
Frequency
selection
Station
selection
Link configuration
Operational State
Health State
Usage State

## Slide 8: Low.CBF MACE correlation model
Sub-array station selection is done near the CBF output
Implementation of the frequency channel processing is hidden in the model. This is divided across the CBF FPGA hardware.
Sub-array X visibilities
selected and tagged for
output to SDP
Stations
Stations
Correlator output products (visibilities)
Notes: Low.CBF

## Slide 9: Low.CBF MACE PSS beamforming model
Low.CSP
Low.LFAA
Low.CBF
LFAA Logical station beam processors
Cross-connect
500 PSS beam-formers
Low.PSS
LMC
Server
Beam weights
Frequency selection
Bandwidth selection
Link configuration
Station selection
Operational State
Health State
Usage State
Notes: Fixed point-to-point fibre links from CBF beamformers to PSS or PST beam processing units. No routing, switching or link input selection.
PSS and PST beam processing unit input is selected through configuration of its associated CBF beamformer

## Slide 10: Focus on LMC-CBF interface
Low.CBF MACE requirement sources are:
  Jama
  “LMC-CSP Sub-elements” ICD, SKA-TEL-CSP-0000019 Sonja Vrcic & Mike MacIntosh 2015-12-11 (Trieste version)
  “Low Telescope ICD CSP to TM”, 100-000000-021 S.Vrcic 2016-03-11.
Assume some LMC-CBF interface flexibility with need for better LMC CBF collaboration to define details.
Notes: Assume “thin LMC” from LMC DDD (SKA-TEL-CSP-000102 Sonja Vrcic 2016-03-15 Trieste version).

## Slide 11: LMC with MACE Architecture – Stage 1
FPGA
Power
Switch
Server
FPGA device
Power device
Switch device
Server device
Protocol 1
Protocol 2
Protocol 3
Protocol 4
Components
Component
software interfaces
Cooling
Cooling device
Protocol 5
Software
Hardware
CSP Element
Capabilities
Fixed TM-LMC
interface
LMC
MACE
Some LMC-CBF interface flexibility
CSP common TM interface
Functionality
Network
Sub-arrays
Beams
System
Notes: Get rid of MC
Cloud - functionality undefined

## Slide 12: MACE functionality from requirements
Functionality derived from TM-LMC and LMC-CBF ICDs. Related functionality grouped together.
  Capability discovery, repair and fault diagnosis
  Configuration parameters GET/SET
  Monitor Points, Events, Alarms and Logging
  Remote power state and upgrades
  User interfaces
  Persistent state
Preliminary agreement to use TANGO [TM-CSP ICD]
  Make architecture able to be implemented using TANGO
  Avoid TANGO “anti-patterns”
Notes: Capability discovery
All objects must have a unique identifier (aka Address) that allows a client to communicate with it
All objects must have a self-describing interface (ie description of Operations and Attributes)
The CBF should be able to provide a list of achievable capabilities. Eg) Exclude FPGA in broken LRUs
Fault status should be persistent
LMC is to be informed when capabilities change
The CBF should be able to suggest and switch to alternative components when there is a fault (eg broken optical fibre)
Configuration parameters GET/SET
Must support configuration of 16 sub-arrays
Must support run-time addition and removal of resources from sub-arrays
Must support pre-defined states and modes – OperationalState, HealthState, UsageState and RedundancyMode
Synchronized activation of configuration across a group of components. Important for recalibration during a scan and concurrent multi-user access
Monitor Points, Events, Alarms & Logging
Events must be sent to the LMC when pre-defined state and mode values are changed by the CBF
Alarms are safety critical events (eg equipment overheating). The status of alarms is persistent and available for further interrogation by the TM. Alarm state is only cleared by TM.
The CBF must log events, alarms and other conditions

## Slide 13: Describing Architecture using UML
LMC describes Element Capabilities such as sub-array and beam. We can define CBF Sub-Element Capabilities too.
We will use UML to describe software architecture.
Communication between objects (eg RPC or Protocol X over Ethernet) is assumed. Can be network or RPC.
Correlator
observingMode
healthState
setObservingMode()
getHealthReport()
Class (Capability) name
Attributes (Parameters)
Operations (Commands)
Example UML Class

## Slide 14: Low.CBF station-processor Capability UML model
Attributes:
version
components
observingMode
activeAlarms
healthState
administrativeMode
operationalState
usageState
redundancyState
delayModels
linkConfig
Operations:
setDelayModels()
setRFIMitigaton()
getHealthReport()
setObservingMode()
configLink()
CbfStationProcessor
One named CbfStationProcessor object per CBF logical station beam processor

## Slide 15: LMC Logical connectivity model for LFAA to CBF
Logical station beam 1
station1 : CbfStationProcessor
Logical station beam 2
Logical station beam N
LFAA
CBF
Logical point-point connections
Mapping of logical connections
to physical fibres undefined
station2 : CbfStationProcessor
stationN : CbfStationProcessor

## Slide 16: Remote power state and upgrades
Remote control over power-on, power-off or transition to low power mode for:
  CSP as a whole
  Specified sub-elements (eg just CBF)
  Specified Components (eg FPGA1).
  Specified LRUs
Staged power-up and delayed power down
Remote firmware or software upgrade (of Components)

## Slide 17: Low.CBF System Capability UML Model
Attributes:
version
components
activeAlarms
healthState
administrativeMode
operationalState
usageState
redundancyState
Operations:
stagedPowerUp()
delayedPowerDown()
getHealthReport()
CbfSystem
Single named object
Power state control for all CBF Components is a single LMC call (eg stagedPowerUp)
Also useful as single point of contact for CBF active Alarms, Component lists and health state
Associated within CBF with persistent state configuration

## Slide 18: LMC with MACE Architecture – Stage 2
TM-LMC interface
LMC-CBF interface
Persistence
User Interfaces
Additional CBF “middle-ware”
Private area (No direct LMC access)
Low.CBF Sub-Element Capability UML Classes
Low.CBF Components
Low.CSP Element Capabilities
CSP common TM interface
Sub-arrays
Beams
System
CbfCorrelator
CbfPssBeamFormer
CbfStationProcessor
CbfPstBeamFormer
CbfSystem
FPGA device
Power device
Switch device
Server device
Cooling device
CbfHardwareProxy
Notes: LMC operations on individual components use the CbfHardwareProxy and go via the CbfSystem Capability.
Some LMC commands are CBF system wide while others may operate on a single Component CbfSystem/CbfHardwareProxy
HardwareProxy:
FPGA, Power, Switch, Server and Cooling Components all “kind of” hardware Components so UML generalization relationship can be made.
Some common operations for all hardware Components. Eg) Power-up, upgrade software/firmware
Some common state and mode support for all hardware Components - administrativeMode, controlMode, simulatedMode, testMode, operationalState, healthState, usageState and redundancyState
Of course it’s a requirement that we support tunnelling into individual Components so that an Engineering interface can access individual registers for troubleshooting purposes.

## Slide 19: Suggested LMC-CBF “Capability interface”
LmcSubArray
CbfCorrelator
1
1
CbfBeamFormer
LMC aware of Low.CBF Capabilities and configuration models
LMC calls CBF Sub-Element Capability objects directly
CBF Capabilities provide model of CBF hardware operation
These would all be implemented as TANGO devices
LMC-CBF
interface
LmcBeam
1
1
CbfPstBeamFormer
CbfPssBeamFormer
CbfSystem
CbfStationProcessor
LmcStation
LmcSystem
1
1
1
1
1
*
1
*
CbfHardwareProxy
1
*

## Slide 20: Getting the LMC-CBF interface right
LMC should delegate control at a Capability level.
LMC control of individual CBF Components is unnecessary in most cases.
Mapping LFAA, PSS and PST connections to individual CBF physical Components is messy. Better for LMC to use logical connection names.
CBF should be aware of group operations (eg Recalibrate sub-array 1 imaging), especially when synchronized activation is required. This allows CBF to optimize shared FPGA functionality and communications.
Each CBF Component type is expected to be configured in a different way (eg FPGAs may use register map and protocol 1, switch may use text commands over SSH). Best if LMC doesn’t have to know these details.
A LMC-CBF “Capability interface” requires less shared knowledge than a Component level interface. The ICD is shorter and implementation cost reduced.
Harmonization across the LMC-CBF interface results in a shorter ICD and reduced implementation cost.
Shorter ICD => Simpler interface => Reduced Cost
Notes: Do you want an ICD filled with arcanly formatted FPGA registers for hundreds of FPGA devices that subtlly change with each firmware version?
This also isolates

## Slide 21: Example Scenario interface messaging: LRU power down following clock synchronization Alarm
f101 : CbfFpga
LMC
: CbfSystem
powerDownLRU
clockSyncFail
clockSyncAlarm
p101 : CbfPower
TM: Power down faulty LRU?
switchOff
clearAlarm

## Slide 22: Next steps – Improving design confidence
Write software simulators for CBF Components
Write prototyping software for CBF Capabilities
De-risk the LMC-CBF interface with LMC prototype software
MACE High-Level Architecture
Software design
CBF software prototyping
LMC-CBF interface validation
LMC prototype

## Slide 23: Questions?