## Slide 1
The upgraded GMRT : A stepping stone towards the SKA
Yashwant Gupta
National Centre for Radio Astrophysics
Pune India
SKA Science Meet 2016 Goa 7 Nov 2016

## Slide 2
Plan of today's presentation
Upgrading the GMRT – goals and plans
Main features of the uGMRT
Developments & current status of different aspects of the uGMRT
Plans for (phased) release of the uGMRT to the user community
Synergy
With
The
SKA
Notes: 2
2

## Slide 3
The existing GMRT : An Overview
30 dishes, 45 m diameter each
  12 dishes in a central 1 km x 1 km region (central square)
  remaining along 3 arms of Y-shaped array
  baselines : ~ 200 m (shortest);
  ~ 30 km (longest)
Frequency range :
  130-170 MHz
  225-245 MHz
  300-360 MHz
  580-660 MHz
  1000-1450 MHz
  max instantaneous BW = 32 MHz
Effective collecting area (2-3% of SKA) :
  30,000 sq m at lower frequencies
  20,000 sq m at highest frequencies
Supports 2 modes of operation :
  Interferometry, aperture synthesis
  Array mode (incoherent & coherent)
Notes: 3

## Slide 4
The existing GMRT : An Overview
30 dishes, 45 m diameter each
  12 dishes in a central 1 km x 1 km region (central square)
  remaining along 3 arms of Y-shaped array
  baselines : ~ 200 m (shortest);
  ~ 30 km (longest)
Frequency range :
  130-170 MHz
  225-245 MHz
  300-360 MHz
  580-660 MHz
  1000-1450 MHz
  max instantaneous BW = 32 MHz
Effective collecting area (2-3% of SKA) :
  30,000 sq m at lower frequencies
  20,000 sq m at highest frequencies
Supports 2 modes of operation :
  Interferometry, aperture synthesis
  Array mode (incoherent & coherent)
14 km
1 km x 1 km
Notes: 4

## Slide 5
Dedication of the GMRT
The Giant Metrewave Radio Telescope was dedicated to the World Scientific Community by the Chairman of TIFR Council, Shri Ratan Tata.
October 4, 2001
Notes: 5

## Slide 6
GMRT : Usage Statistics
GMRT sees users from all over the world : distribution of Indian vs Foreign users is close to 45:55
The GMRT has been typically oversubscribed by a factor of 2 or more
Notes: 6
6
6

## Slide 7: GMRT : Scientific Objectives
The GMRT is a powerful instrument to probe several astrophysical objects and phenomena :
  The Sun, extrasolar planets
  Pulsars : rapidly rotating neutron stars
  Other Galactice objects like : supernova remnants, microquasars etc
  Other explosive events like Gamma Ray Bursts
  Ionized and neutral Hydrogen gas clouds (in our Galaxy and in other galaxies)
  Radio properties of different kinds of galaxies; galaxy clusters
  Radio galaxies at large distances in the Universe
  Cosmology and the Epoch of Reionization
  All sky surveys such as the 150 MHz TGSS
  …and many interesting new results have been produced

## Slide 8
Next Generation : The uGMRT
For last several years the GMRT has been working well on the global stage; however, it was time to think of the future & upgrade the facility, keeping in mind technology development for global efforts such as the SKA.
Main goals for the upgraded GMRT (uGMRT) were identified as :
  Seamless frequency coverage from ~ 50 MHz to 1500 MHz, instead of the limited bands at present  design of completely new feeds and receiver systems with ~ octave bandwidths
  Improved dynamic range and G/Tsys  better technology receivers
  Increased instantaneous bandwidth of 400 MHz (from the present maximum of 32 MHz)  new digital back-end receiver
  Revamped servo system  brushless drives, new servo computer etc
  Modern, versatile control and monitor system  SKA contribution
  Matching improvements in offline computing facilities
  Improvements in mechanical & electrical systems, infrastructure facilities
  To be done without compromising availability of existing GMRT to users
Notes: 8
8

## Slide 9
uGMRT : Expected Performance
Expected sensitivity performance of the upgraded GMRT compared to other major facilities in the world, present and projected (courtesy : Nissim Kanekar, NCRA)
Spectral lines : broadband coverage will give significant increase in the redshift space for HI lines + access to other lines
Continuum imaging sensitivity will improve by factor of 3 or so.
Sensitivity for pulsar observations will also improve by factor of 3.
Only SKA-I will do better then uGMRT at centimeter wavelengths

## Slide 10
Overview of uGMRT Receiver System
Broad-band feeds + FE (in octaves) :
  1000 – 1450 MHz (updating L-band)
  550 – 900 MHz (replacing 610)
  250 – 500 MHz (replacing 325)
  120 – 250 MHz (replacing 150)
Modified optical fibre system to cater to wideband (50 to 2000 MHz) dual pol RF signals (while allowing existing IF signals)
Analog back-end system to translate RF signals to 0 - 400 MHz baseband
Digital back-end system process 400 MHz BW for interferometric and beam modes

## Slide 11
Wideband feeds + FE for uGMRT : L-band system – “Band 5”
For this band, we are going with the existing broadband L-band feed : ~ 900 to 1450 MHz (usable from ~ 1000 MHz upwards due to mobile phone RFI)
Improved LNA (higher dynamic range) + better filters for rejecting RFI
30 antenna system completed more than one year ago; some refinements of filters planned in 2nd phase of improvement
Sufficient sets of spares in hand now.
This system is FULLY READY !
Notes: 11

## Slide 12
Wideband feeds + FE for uGMRT : L-band system (Band-5)
Performance of Lband system is monitored regularly by FE team to keep the system in good health – need to watch out for growing RFI also.
Notes: 12

## Slide 13
Wideband feeds + FE for uGMRT :
550-900 MHz system – “Band 4”
Replaces existing 235/610 system
Front-End system split into two parts :
Polariser + LNA is right next to feed (to minimize the loss)
Rest of the FE electronics is in the regular box
Now installed on 10 antennas and growing…
Cone Dipole feed (for 550-900)
alongwith polarizer and LNA
Notes: 13

## Slide 14
Wideband feeds + FE for uGMRT :
550-900 MHz system – “Band 4”
Performs better than existing feed at 610 MHz
Nice, clean band with negligible RFI
Notes: 14

## Slide 15
Wideband feeds + FE for uGMRT : 250-500 MHz system – “Band 3”
Replaces existing 325 MHz system
Broad-band (250-500 MHz) feed with good E-H pattern match
Upgraded wideband FE system with new LNA : improved Tsys (22 vs 36 K) & dynamic range
Up on 29 antennas – will complete all 30 next week !
Cone Dipole feed (250-500) and
FE box
Notes: 15

## Slide 16
Wideband feeds + FE for uGMRT : 250-500 MHz system (Band 3)
Performance of Band-3 system is monitored regularly by FE team – system is in good health.
Need to watch out for growing menace of RFI.
Notes: 16

## Slide 17
Wideband feeds + FE for uGMRT :
120-250 MHz system -- “Band 2”
Broad-band feed for 120-250 MHz in final acceptance phase, installed on 4 antennas
Sensitivity : at 150 MHz -- better than existing system; at 235 MHz -- comparable to existing system
Dual Ring Feed : 130-260 MHz
Notes: 17

## Slide 18
uGMRT : New Wideband Systems
Summary
Proposed configuration of feeds and receivers and their current status :
  Band 5 (1000 – 1450 MHz ) : existing wideband feed + improved dynamic range rx with appropriate RFI filters -- completed on 30 antennas.
  Band 4 (550 – 900 MHz) : cone-dipole feed with matching receiver system finalized and now in mas production phase -- 10 antennas completed.
  Band 3 (250 – 500 MHz) : cone-dipole feed + receiver is well into mass production & installation -- 29 antennas completed.
  Band 2 (120 – 250 MHz) : modified Kildal ring feed + modified electronics in last stages of validation – populated on 4 antennas.
  Band 1 (50 – 80 MHz) : on hold at present.
Notes: 18
18
18

## Slide 19
Overview of uGMRT Receiver System
Broad-band feeds + FE (in octaves) :
  120 – 250 MHz (replacing 150)
  250 – 500 MHz (replacing 325)
  550 – 900 MHz (replacing 610)
  1000 – 1450 MHz (updating L-band)
Modified optical fibre system to cater to wideband (50 to 2000 MHz) dual pol RF signals (while allowing existing IF signals)
Analog back-end system to translate RF signals to 0 - 400 MHz baseband
Digital back-end system process 400 MHz BW for interferometric and beam modes

## Slide 20
OTX 1550.11 nm (193.4 THz)
OTX 1548.51 nm (193.6 THz)
ORX 1550.11 nm
ORX 1548.51 nm
1551.72 nm
(193.2 THz)
1553.32 nm
(193.0 THz)
1551.72 nm
1553.32 nm
DWDM Multiplexer
at Antenna Base
DWDM de-Multiplexer at CEB
Fiber link
22.9 km
GMRT Upgrade : Optical Fibre Systems
DWDM based, broad-band (2.5 GHz), analog optical fibre transmission scheme; features : 20 dB S/N; 40 dB dynamic range
Will bring back 2 broad-band RF channels + existing IF channels ; will also support new and existing control and monitoring schemes
Notes: 20

## Slide 21
GMRT Upgrade : Optical Fibre Systems
Completed installation for all 30 antennas in September 2015 and working well
Notes: 21

## Slide 22
Overview of uGMRT Receiver System
Broad-band feeds + FE (in octaves) :
  120 – 250 MHz (replacing 150)
  250 – 500 MHz (replacing 325)
  550 – 900 MHz (replacing 610)
  1000 – 1450 MHz (updating L-band)
Modified optical fibre system to cater to wideband (50 to 2000 MHz) dual pol RF signals (while allowing existing IF signals)
Analog back-end system to translate RF signals to 0 - 400 MHz baseband
Digital back-end system process 400 MHz BW for interferometric and beam modes

## Slide 23
uGMRT : Analog Backend
Receives wideband RF signals from OF system output
Converts to baseband signals of 100, 200, 400 MHz BW after appropriate signal conditioning (amplification, filtering etc)

## Slide 24
uGMRT : Analog Backend Status
Phase-I 30-antenna system installation completed ; peripheral units under installation as part of phase-II

## Slide 25
Overview of uGMRT Receiver System
Broad-band feeds + FE (in octaves) :
  120 – 250 MHz (replacing 150)
  250 – 500 MHz (replacing 325)
  550 – 900 MHz (replacing 610)
  1000 – 1450 MHz (updating L-band)
Modified optical fibre system to cater to wideband (50 to 2000 MHz) dual pol RF signals (while allowing existing IF signals)
Analog back-end system to translate RF signals to 0 - 400 MHz baseband
Digital back-end system process 400 MHz BW for interferometric and beam modes

## Slide 26
uGMRT Digital Backend :
Hybrid Correlator Design
Antenna 32
(400 MHz
2 pols)
ADC
(2channels)
FPGA
(packetizer)
CPU + GPU
(correlator)
Switch
(40 Gbe)
Antenna 1
(400 MHz
2 pols)
ADC (2channels)
FPGA
(packetizer)
CPU + GPU
(correlator)
Antenna 2
(400 MHz
2 pols)
ADC
(2channels)
FPGA
(packetizer)
CPU + GPU
(correlator)
Data Acquisition and Control
CPU + GPU
(correlator)
CPU + GPU
(correlator)
CPU + GPU
(correlator)
32 stations, 400 MHz BW, 16-32 K channels,
Full Stokes correlator + beamformer + pulsar rx.

## Slide 27
GWB-III : 16 antenna (dual poln) 400 MHz software backend for the uGMRT
8-node GPU system
16 ADC cards + 8 FPGA boards
Dual K20 GPUs on each T620 node
Released in September 2015
BW : 400 MHz, upto 16K channels
Int Time : 0.67 sec
IA/PA Beamformer
Upgrade to 32 stations by Nov 2016

## Slide 28
Towards a working uGMRT…
Notes: 28

## Slide 29
3C129 imaged with the uGMRT system using 14 antennas, 200 MHz BW
uGMRT : Early Sample Results
courtesy : Dharam Vir Lal + Binny Sebastian

## Slide 30
GHB: 4 hrs, BW: 14 MHz, rms=55 microJy/beam
GWB: 2 hrs, BW: 250 MHz, rms=30 microJy/beam
uGMRT : Early Sample Results
courtesy : C.H. Ishwara-Chandra + Binny Sebastian
Imaging with the 400 MHz bandwidth mode at Lband

## Slide 31
Wideband pulsar observations
PSR B1508+55
300-500 MHz band
(200 MHz BW)
Using 8 antennas
Phased Array mode.
Notes: 31

## Slide 32
Wideband pulsar observations : improved sensitivity
PSR B1508+55
120 MHz at Lband (1330-1450)
vs
33 MHz at Lband (1390 sub-band)
Simultaneous observations using same # of antennas in phased array mode.
Notes: 32

## Slide 33
Pulsar timing results with uGMRT
courtesy : Nikhil Naik & Y. Gupta
Regular timing observations for a few well known pulsars at multiple frequencies to test the system – appears to be working quite well
Recently started regular program of monitoring a set of MSPs for precision timing
Timing residuals for 3 frequency observations for test pulsar B0138+59
Initial results for timing residuals for MSP B1855+09
Notes: 33
33

## Slide 34
Wideband Coherent Dedispersion for the uGMRT
courtesy : Kishalay De & Y. Gupta
Coherent Dedispersion on voltage output of phased array mode of uGMRT
Working in real-time (GPUs), for 100 to 200 MHz BWs, at low frequencies.
Will be released soon for the general user community.
Will increase the quality of pulsar timing with the uGMRT
Comparison of
regular phased array beam output
with
coherent dedispersion output
for 300 to 500 MHz band of the uGMRT, for PSR J0613-0200
Notes: 34
34

## Slide 35
Upgraded GMRT : opening new windows – Band 3
First light results : spectral lines from different sources, at different parts of the 250-500 MHz band (Nissim Kanekar)
Notes: 35

## Slide 36
Upgraded GMRT : opening new windows – Band 4
First light results : spectral lines from different sources, at different parts of the 550-900 MHz band (Nissim Kanekar)
Notes: 36

## Slide 37
Challenges on the Road to uGMRT
The main challenges that we have encountered have been :
Technological : design of the wideband receiver systems was a major challenge
Operational : keeping the existing GMRT working for our regular users while upgrading simultaneously took some effort
Taking care of man made Radio Frequency Interference (RFI) is and remains our biggest challenge !
  Containing self generated RFI
  Mitigating RFI from external sources :
  (i) broadband impulsive (ii) spectral line
Notes: 37
37

## Slide 38
Ongoing & Future Plans for uGMRT
Mitigating Radio Frequency Interference (RFI)
Real-time coherent dedispersion
Gated correlator
Real-time fast transient pipeline
New monitor & control system as a SKA prototype
Notes: 38
38

## Slide 39
External Sources of RFI
Notes: 39
39

## Slide 40
Avoiding RFI from satellites
Real-time prediction of positions of known satellites (stationary and moving)
Real-time warning when observing antenna beam comes within zone of avoidance (decided by beamwidth and strength of satellite)
Predictive warning : can work on your submitted observing file
Post-facto warning : can work on your recorded data file
Notes: 40
40

## Slide 41
uGMRT : RFI Detection & Filtering
Real-time filter running on broadband voltage data of each antenna
Real-time spectral line filter running on spectra from each antenna
Real-time filter running on time-frequency visibility data (planned)
Real-time filter on time & frequency data of beamformer data stream.
Notes: 41
41

## Slide 42
42
RFI mitigation in digital domain
FPGA Implementation
RF @ 150MHz (Blue) and 3σ clipped (Red)
Median Absolute Deviation (MAD) based flagging of RFI
Detection followed by filtering and clipping the value at the threshold or replacement with random noise or median value
Can detect broadband random noise spikes (e.g. powerline RFI) in real-time on dedicated FPGA hardware
Is being integrated into the main correlator design; trial version will be released soon.
Notes: 42
42

## Slide 43
Real-time RFI Detection & Filtering
Real-time filter running on broadband voltage data of each antenna
Top panel shows effect of this filtering, in beamformer time series
Bottom panels show effect of this filtering, in visibility domain data
Notes: 43
43

## Slide 44
Real-time RFI Detection & Filtering
Real-time filtering of time-frequency of beamformer data – now available
courtesy : A. Chowdhury
Notes: 44
44

## Slide 45
Some fun stuff :
Tracking Space Probes with the uGMRT !
Ground support for ExoMars mission of ESA
GMRT + NASA collaboration
Faithfully tracked ESA’s Schiaparelli Lander module : ~ 3 W signal @ 401 MHz from Mars !
Notes: 45
45

## Slide 46
Release of uGMRT to Users
Releases in multiple phases :
1. First release of 8 antenna trial system – way back in September 2013.
2. Release of 16 antenna system for internal users – September 2015.
3. Release of 16 antenna system for all users -- April 2016 .
4. Now happening : Release of a 30 antenna system with 2 bands fully functional : Band 5 (1000 to 1450 MHz) and Band 3 (250-500 MHz) -- October-November 2016 (GTAC Cycle 31)
5. In the future : Release of fully upgraded GMRT : 30 antenna configuration with all 4 bands fully functional -- September 2017.
 This is well positioned in time to provide valuable learnings for science with the SKA
Notes: 46
46

## Slide 47
Summary
Questions ?
In terms of capabilities,
techniques,
science potential,
timeline of realization,
the uGMRT is well positioned as
as a stepping stone to the SKA - I
Notes: 47