## Slide 1
CSP_Low.LMC Data Rates
Grant Hampson and John Bunton
11th August 2016

## Slide 2: Overview
For Low.CBF data rates are dominated by beamformer weights and calibration data
Other types of LMC data:
Static RFI blanking tables
Sub-element monitoring (V, T, P, O, signals, etc.)
General controls (delay, configuration, dynamic RFI, etc.)
Refresh rate relatively slow
Look more closely at beamformer …

## Slide 3: Beamformer Control loop
CSP_Low.PST
SDP
TM
CSP_Low.CBF
CSP_Low.PSS
CSP_Low.LMC
SDP has all the information required to calculate beamformer weights and calibration for Low.CBF
Assume weights/cal goes via TM, schedule for a give time
Sets weights/cal in Low.CBF, at a given time
SADT is everywhere transporting this data
Generates calibrated beams. Floats converted to fixed point values
Analyses beams
Floats
Floats
Floats

## Slide 4: PST LMC Size
Assumptions:
Jones matrix applied per coarse channel, station and beam
Weights are phase only and scale with frequency (gain is in Jones). Same phase for both polarisations
PST Jones Matrix | Coarse | 384 | 
 | Stations | 512 | 
 | Beams | 16 | 
 | Real values | 8 | per matrix
 | Bits | 12 | 
 |  | 301989888 | Bits
PST Beamformer | Coarse | 1 | Single phase calculate for lowest frequency and multiply up
 | Stations | 512 | 
 | Polarisations | 1 | Same value for each polarisation
 | Beams | 16 | 
 | Real values | 2 | Phase slope and intial value (calculate exact frequency)
 | Bits | 16 | 
 |  | 262144 | Bits

## Slide 5: PSS LMC Size
Assumptions:
Station Jones matrix applied per coarse channel and station (same for all beams)
Weights are phase only and scale with frequency (gain is in Jones). Same phase for both polarisations.
Beam Jones matrix applied per coarse channel and beam
Station Jones Matrix | Coarse | 384 | 
 | Stations | 512 | 
 | Beams | 1 | Same for all beams
 | Real values | 8 | per matrix
 | Bits | 12 | 
 |  | 18874368 | bits
PSS Beamformer | Coarse | 1 | 
 | Stations | 512 | 
 | Polarisations | 1 | Same value for each polarisation
 | Beams | 500 | 
 | Real values | 2 | Phase slope and intial value (calculate exact frequency)
 | Bits | 16 | 
 |  | 8192000 | bits
PSS Beam Jones Matrix | Coarse | 384 | 
 | Beams | 250 | per beam correction
 | Real values | 8 | per matrix
 | Bits | 12 | 
 |  | 9216000 | bits

## Slide 6: LMC data rates
Assumptions:
Fasted update rate is 1-second
Overall LMC rate is 339Mbps
Assume 48-FPGAs in beamformer – and inefficiency in coarse channel distribution, then datarate per FPGA is 42Mbps
Total PST bits | 302252032 | bits
Total PSS bits | 36282368 | bits
Total bits | 338534400 | bits
Update rate | 1 | seconds
Data rate | 339 | Mbps
FPGAs | 48 | 
Data rate / FPGA | 7052800 | 
 | 7 | Mbps
Inefficiency | 6 | BF Fine channel split means there is inefficiency as same coarse channels appear in 6 BF FPGAs
Data rate/FPGA | 42 | Mbps

## Slide 7: Storm in a teacup
Had impression rates much higher!
Overheads not included – such as floats in majority of network (increase rates by 32/12=266% = 1Gbps)
Like to validate Low.CBF assumptions though to ensure correct:
Could change datarate dramatically
Ensure beamformer weight and calibration path is correct
Bit widths are appropriate

## Slide 8: Questions?