## Slide 1: SKA LOW 2022 Meeting
Overview of Station Calibration using EEPs
Ravi Subrahmanyan [S&A CSIRO, Curtin-CIRA]
8 February 2022

## Slide 2: AAVS2 embedded element patterns
Mutual coupling between antennas in the station. Results in distortions to the beam patterns of the embedded antennas.
Embedded Element Patterns (EEPs):
Complex, direction-dependent, voltage patterns of the X & Y polarized feeds: their response to
H and V sky polarization.

## Slide 3
X-pol
Y-pol
EEPs @ 110 MHz
(antenna power patterns)
Calibration needs to take into account the direction-dependent antenna gains

## Slide 4: Sky Model: GSM+Sun
Healpix Global Sky Model
[Zeng ++ 2016; PyGSM]
Degraded to 1.8 deg resolution (nside=32 healpix) as model for 110 MHz AAVS2
Sun added in at each timestamp in appropriate pixel with pixel-averaged temperature
Sun flux density from [Benz 2009]

## Slide 5: Measurement data
110 MHz AAVS2
21/22 April 2020 – 250 functioning antennas (6 faulty antennas)
Intra-station correlations XX, YY for all 31125 baselines
Frequency averaged over 0.926 MHz coarse channel
Time averaged to give integration time 0.28 sec
Snapshot observations available every 5 mins.

## Slide 6: Calibration of XX, YY autocorrelations (110 MHz):
Plot measured XX, YY Counts versus predicted XX, YY antenna temperature.
Fit straight line to get offset (Treceiver) and slope (gain: counts/K).
Apply the additive and multiplicative calibration factors to each antenna
Mean of the fit offsets: 40 K
(consistent with expectation for receiver noise temperature)
X-pol
Y-pol

## Slide 7: Comparison: calibrated XX, YY autocorrelations versus predicted antenna temperatures (using EEPs)
X-pol
Y-pol
Verifies connectivity, configuration,
basic performance, EM models

## Slide 8: Residual gain variations over the day/night:
X-pol
Y-pol
Calibration with EEPs has the potential to reveal intra-station gain drifts.
Gain variations are more in day compared to night; more in X compared to Y.
Differing in antennas serviced by same SMART boxes.

## Slide 9: Calibrations of XX & YY cross correlations (110 MHz):
Predict visibility amplitudes/phases on all baselines/times:
3D FT from l,m,n of pixels in healpix sky to u,v,w of baselines
Correct for direction dependent complex gains of antennas forming the baseline – this is a complex correction for each pixel, each baseline, each polarization.
Sky model + Sun assumed unpolarized.

## Slide 10
Measured (uncalibrated)
Visibility amplitudes
Predicted (kelvin units)
Visibility amplitudes
At time when GC is at zenith
At time when Sun transits the meridian

## Slide 11: Antenna-based gain solutions
Comparing the 31125 baseline visibility predictions & measurements.
XX and YY correlations separately
Solving for 250 amp/phs gain solutions independently at each time
Using MIRIAD SELFCAL. Although this is “calibration” and not “self-calibration”
Removing common mode gain drifts – which do not affect station beamforming

## Slide 12
Antenna-based intrastation gain solutions
Amplitude gains
X-pol
STD = 0.059
Y-pol
STD = 0.060

## Slide 13
Antenna-based intrastation gain solutions
Phase gains
X-pol
STD = 5.99 deg
Y-pol
STD = 6.06 deg

## Slide 14: Comparison of gain solutions: EEP vs Average EEP

## Slide 15: Calibrated visibilities: Model versus Data
At time when
Sun transits the meridian

## Slide 16: Calibrated visibilities: Model versus Data
At time when
GC transits the meridian

## Slide 17: Comparison of calibrated data & model visibility versus UT on shortest baselines 0.5-0.7 wavelengths 1.4-1.9 metres

## Slide 18: All-sky image in Stokes I: Made as 3D transform from u,v,w at all times to a common drifting healpix sky Using the EEPs to compute the direction-dependent complex gains for each baseline

## Slide 19
Summary:
Antenna amplitude calibration to within 3% RMS accuracy is possible using predictions from GSM + Sun + EEPs.
Intra-station complex gains are stable over the day/night to within 6%, 6 deg std.
Complex gain solutions are possible in snapshot data at all LSTs – to within this accuracy – using GSM + Sun + EEPs. Quantifying the accuracy of calibration is work in progress.