## Slide 1: SKA MID: Technical Challenges
Robert Laing
MASUM - May 10 2022

## Slide 2: Improving the Design Baseline
System analysis and performance (test and simulation): what doesn’t work (yet)?
Has the external environment changed: what’s different?
One example of each
Notes: One example of each. No attempt to be comprehensive.

## Slide 3: What doesn’t work (yet)?
Dish pointing

## Slide 4: Basic Interferometry with Dish Arrays
Resolution (rad) ≈ λ/dmax (λ = wavelength, dmax = maximum baseline)
Field of view (rad) ≈ λ/D (D = dish diameter)
Largest scale of structure ≈ λ/dmin (dmin = minimum baseline; slightly larger than D)
Noise level ∝ D-2[N(N-1)ΔνΔt]-1/2 (N = number of dishes, Δν = bandwidth, Δt = observing time)
Image fidelity increases with the number of baselines, N(N-1)/2.
Optimisation of performance and cost → N = 197, D = 15 m, dmax = 150 km
We have to point the dishes to a small fraction of λ/D.

## Slide 5: Offset Gregorian Optics
Pro:
  Unblocked aperture
    Smooth, azimuthally symmetric beam
    Low scattering and spillover noise
  High efficiency
  Space at the focus for multiple receiver bands
Con:
  Not as stiff as classical Cassegrain design
  Harder to maintain pointing
Notes: Concave paraboloid + ellipsoid

## Slide 6: Why do we need good pointing?
We want to map the sky brightness I(l,m) where l and m represent direction on the sky
A perfect interferometer between dishes 1 and 2 measures the visibility
V(u,v) = ∫∫I(l,m) exp[-2πi(ul+vm)] dl dm
(u, v are the baseline coordinates).
In practice, we need to include the response of the interferometer element (dish), so we end up measuring
I(l,m) D1(l,m)D*2(l,m)
where D1 and D2 are the responses of the two dishes.
This is fine if we know D1 and D2 exactly, but not otherwise.
Various effects cause D1 and D2 to vary unpredictably with time: pointing errors (e.g. due to wind), dish deformations (gravity, thermal), ionosphere.
Notes: If D1 andD2 are the same, can simplify. Also helps if they have no azimuthal dependence.

## Slide 7: What happens in real observations?
Imaging artefacts
Increased noise level
Correction in post-processing
is theoretically possible, but
tricky in practice
Deliberately mispointed
WSRT observation
Notes: Explain why calibration is hard: time variable; beam not well enough known.

## Slide 8: Computing the effects of pointing errors
Error models (per dish; correlated or random)
  Dynamic pointing error due to wind, assuming constant direction and variable speed
  Static pointing error
Models for beam, sky and array layout
Compute interferometric visibilities with and without pointing errors
Difference
Image → Metric is rms noise on the difference image

## Slide 9: Results (Maciej Serylak)
Source model Pointing errors Image errors
Given a distribution of pointing errors (in this case too optimistic),
we can compute imaging errors for a typical field

## Slide 10: This is where the L1 Requirements come from:
Blind pointing <9, 18, 36 arcsec rms (precision, standard degraded conditions)
Relative pointing (10o separation) <1.3, 2.6, 5.2 arcsec rms
Tracking <2.3, 4.6, 9.2 arcsec rms
These specifications can easily be met by Cassegrain, CFRP antennas designed for mm wavelengths (ALMA): the challenge is to achieve them with a steel, offset Gregorian design at much lower cost.
→ Ockert’s talk

## Slide 11: What’s different?
Satellite Mega-constellations
(slides from Federico di Vruno)

## Slide 12: Satellite Mega-Constellations
Low Earth Orbit
  Very large number of satellites
  Starlink, OneWeb, …
Allocated frequency range in Band 5b
  10.7- 12.75 GHz: large fraction of the band (8.3-15.4 GHz)
Impacts on radio astronomy
  I: High power into analogue/digital signal chain
  II: RFI in wide-band observations (line and continuum)

## Slide 13
Need increased dynamic range in digitizer

## Slide 14: Mitigation
Satellite RFI is not a new situation for radio astronomy:
  Satellite prediction/avoidance
  On- and off-line processing
  Interferometers less vulnerable
Regulation
  No direct satellite downlinks within a defined radius of observatory (Germany, Spain)

## Slide 15: Mitigation 1: Prediction – needs accurate orbital elements

## Slide 16: Mitigation 2: Flagging
Incoherent RFI
  Increases system temperature
  Lower effective bandwidth and sensitivity
Coherent RFI
  Persists after correlation
  Imaging artefacts
  Mitigate with algorithms like AOFlagger (sum-threshold)

## Slide 17: Mitigation 3: Decoherence on long baselines

## Slide 18: Mitigation 4: Keep-out Areas

## Slide 19: High power into receivers with a keep-out zone

## Slide 20: Questions?